Goal: To determine the time domain response of the transfer function

Direct Form 1

Direct Form II

Octave filter

Testcase
The first signal x is 3 sine waves 50, 120, and 300 Hz

The 2nd is the FFT of the signal x.

The 3rd is the filterd with the Butterworth filter.

The 4th show that only the 50 & 120 Hz are present.

Starting first with order 2
a = 1.00000 -0.98241 0.34767

b = 0.091315 0.182630 0.091315

[A,B,C,D] = tf2ss(b,a);

A =

   5.5511e-17 3.4767e-01
  -1.0000e+00 9.8241e-01

B =

  -0.059568
   0.272338

C =

   0 1

D = 0.091315

butt6120lp
normalize freq
nf = 0.24000
zeros
ans =

  -1
  -1
  -1
  -1
  -1
  -1

poles
ans =

   0.61925 + 0.56170i
   0.49120 + 0.32617i
   0.43881 + 0.10665i
   0.43881 - 0.10665i
   0.49120 - 0.32617i
   0.61925 - 0.56170i

theta =

   0.73670
   0.58617
   0.23842
  -0.23842
  -0.58617
  -0.73670

b
b =

 Columns 1 through 6:

   0.00085754 0.00514522 0.01286305 0.01715073 0.01286305 0.00514522

 Column 7:

   0.00085754

a
a =

   1.000000 -3.098542 4.416437 -3.556586 1.685139 -0.441124 0.049558

FFT 50 120 300

delta f	0.48828125	samples	2048	fs	1000

sample = 10*(sin(2*pi*50*t[i]) + sin(2*pi*120*t[i]) + sin(2*pi*300*t[i])); //no DC

( 2.104689, 0.000000)	102	49.8046875
( 7.311564, 0.000000)	103
( 4.836622, 0.000000)	104

( 2.750056, 0.000000)	246	120.1171875
( 8.715654, 0.000000)	247
( 1.689716, 0.000000)	248

( 2.071553, 0.000000)	614	299.8046875
( 7.257226, 0.000000)	615
( 4.845451, 0.000000)	616

https://www.youtube.com/watch?v=vikFFw6Hn0o

Ao Maximum gain in passbands
|H(w)| normalized gain	w = 2pif wo = fo
wo Lower cutoff angular freqency (HPF)
upper cutoff angular freqency (LPF)
angular freqency of input signal
n order(interger 1,2,3…)

bw2.png

bw3.png

bw4.png

bw5.png